## Slide 1
CONDITION BASED MAINTENANCE (CBM)
Fleet Health & Risk Scoring Methodology
Alignment with SBM LOD2-PM, IFS RAM Severity & CBMnet Standards
Reliability & Condition Monitoring Engineering Team | Technical Validation Deck
© SBM Offshore. All rights reserved. www.sbmoffshore.com

## Slide 2
Baseline Context: SBM LOD2-PM & CBMnet Standards
© SBM Offshore. All rights reserved. www.sbmoffshore.com
2
SBM LOD2 - PM Standard
• Activation Logic: Activated when PM is overdue; deactivated upon 'Work Done'.
• FAR Score Determination: Likelihood × RAM-based Severity.
• PM Overdue Mathematical Formula (FAR Standard): PM Overdue (%) = [(Today - Due Date) / PM Interval] × 100%
• Operational Alignment: SBM's LOD2-PM governs collection adherence. We map this directly into our 6 overdue indices (Not Overdue to >200%).
CBMnet Theoretical Standard (§1.6)
• Fault Risk (Max 25): Highest Likelihood of all Faults (Max 5) × Consequence of Failure (Max 5).
• Compliance Risk (Max 25): Compliance Level (Max 5) × Consequence of Failure (Max 5).
• CBMnet Total Risk (Max 30): Fault Risk + (20% × Compliance Risk)
• Core Pareto Weighting Principle: Physical condition is the primary driver of risk. Overdue PM acts as a 20% modifier, preventing admin delays from masking mechanical failures.

## Slide 3
KPI 1: Fault Risk Formulation & Matrix (1 to 12)
© SBM Offshore. All rights reserved. www.sbmoffshore.com
3
FAULT RISK FORMULA = Worst Condition Tier (1 to 4) × IFS RAM Criticality (1 to 3)
Scale: 1 to 12 pts | Multi-Technique Rule: Condition = max(Vibration Tier, Lube Oil Tier)
Fault Risk Matrix (4×3)
IFS Criticality | Tier 4 (Good) | Tier 3 (Good) | Tier 2 (Degr.) | Tier 1 (Crit.)
High / SECE (3) | 3 | 6 | 9 | 12
Medium (2) | 2 | 4 | 6 | 8
Low (1) | 1 | 2 | 3 | 4
Fleet Overall Health % Deduction
• Maximum Fleet Potential: N machines × 12 points
• Active Defect Penalties Only: - Tier 1 (Critical) Machine: Deducts its Fault Risk score - Tier 2 (Degraded) Machine: Deducts its Fault Risk score - Tier 3 / Tier 4 (Good) Machines: Deduct 0 points
• Fleet Health % Formula: Health % = [(Max Points - Deductions) / Max Points] × 100%

## Slide 4
KPI 2: Compliance Risk & PM Overdue (0 to 15)
© SBM Offshore. All rights reserved. www.sbmoffshore.com
4
COMPLIANCE RISK = IFS RAM Criticality (1 to 3) × PM Overdue Index (0 to 5)
Scale: 0 to 15 pts | PM Overdue (%) = [(Today - Planned Date) / PM Interval] × 100%
Compliance Risk Matrix (3×6)
IFS Criticality | Idx 0 (0%) | Idx 1 (50%) | Idx 2 (100%) | Idx 3 (150%) | Idx 4 (200%) | Idx 5 (>200%)
High / SECE (3) | 0 | 3 | 6 | 9 | 12 | 15
Medium (2) | 0 | 2 | 4 | 6 | 8 | 10
Low (1) | 0 | 1 | 2 | 3 | 4 | 5
Fleet Compliance % Deduction
• Maximum Fleet Potential: N machines × 15 points
• Worst-Case Dual Technique Rule: Compliance Risk = max(Crit × Index(Vib), Crit × Index(Oil)) • Overdue Penalty Deductions: Every machine with overdue > 0% subtracts its Compliance Risk score (up to 15 pts).
• Fleet Compliance % Formula: Compliance % = [(Max Points - Deductions) / Max Points] × 100%

## Slide 5
KPI 3: CBM Total Risk Synthesis (1.0 to 15.0)
© SBM Offshore. All rights reserved. www.sbmoffshore.com
5
CBM TOTAL RISK = Fault Risk (1 to 12) + (20% × Compliance Risk (0 to 15))
Scale: 1.0 to 15.0 pts (Minimum: 1.0 | Maximum: 12 + 0.2×15 = 15.0 pts)
Risk Severity Classification Tiers
Range: < 4.0
Asset operating normally within baseline vibration & oil thresholds. Routine surveillance cycle.
LOW RISK
Range: 4.0 - 7.9
Early-stage mechanical degradation or moderate overdue PM. Engineering monitoring review.
MEDIUM RISK
Range: 8.0 - 11.9
Substantial degradation (Tier 2 on critical machine) or severe inspection blind spot. Priority triage.
HIGH RISK
Range: ≥ 12.0
Imminent failure potential (Tier 1 on high criticality machine). Immediate offshore intervention required.
CRITICAL RISK

## Slide 6
Score Harmonization & Fleet Dashboard
© SBM Offshore. All rights reserved. www.sbmoffshore.com
6
Equipment Details Modal: Score Format
UNIFIED RATIO FORMAT IN ASSET HEADER:
[ Fault: 8/12 ] [ Compliance: 6/15 ] [ Total Risk: 9.2/15 ]
Fleet KPI Dashboard Cards (100% Potential)
FAULT RISK & HEALTH
98.3%
HEALTH
Avg Fault Risk: 2.1 / 12 Evaluated: 104 machines At Risk: 3 machines (1 Crit, 2 Deg) Deduction: -21 pts
COMPLIANCE RISK
95.8%
COMPLIANCE
Avg Compliance: 0.8 / 15 On Schedule: 92 machines Overdue PM: 12 machines Deduction: -65 pts
CBM TOTAL RISK
97.2%
TOTAL HEALTH
Avg Total Risk: 2.3 / 15 Critical / High: 2 machines Medium / Low: 102 machines Deduction: -34.0 pts

## Slide 7
Practical Case Study: Crude Export Pump (P-01A)
© SBM Offshore. All rights reserved. www.sbmoffshore.com
7
Asset Condition & Surveillance Inputs
• Asset Tag: P-01A (Crude Oil Export Pump)
• IFS EAM RAM Criticality: High (Score = 3) Single-point production export consequence.
• Surveillance Condition: - Vibration Survey: Tier 2 (Degraded, inner race bearing defect = 3) - Lube Oil Survey: Tier 4 (Good = 1) - Resolved Worst Condition = Tier 2 (Degraded = 3 pts)
• Overdue PM Calculation: - Vibration PM Frequency: 24 days - Last Survey Completed: 42 days ago - Overdue Days: 42 - 24 = 18 days - Overdue %: (18 / 24) × 100% = 75.0% - 75% in (50%-100%] -> Overdue Index = 2
Calculated Risk Scores & Fleet Impact
1. Fault Risk Score:
3 (Crit) × 3 (Tier 2) = 9 / 12 pts
High Risk (橙) — Deducts 9 pts from fleet fault health
2. Compliance Risk Score:
3 (Crit) × 2 (Index) = 6 / 15 pts
Moderate Delay (黄) — Deducts 6 pts from fleet compliance
3. CBM Total Risk Score:
9 + (0.20 × 6) = 10.2 / 15.0 pts
High Risk (橙) — Deducts 10.2 pts from fleet total health
4. Fleet Governance Value:
Zero Ambiguity & Full Traceability
Every deduction point is directly auditable to the bearing defect report and 18-day collection delay.